## Slide 1: UCL – K110 Status Report
Standaert Laurent
UCL- Cyclotron Resource Centre
XXXIX ECPM

## Slide 2: UCL-CRC cyclotron
First beam : 1974
K 110 :
  Radius = 93 cm
  B ≈ 1.6T
Frequency
  11-18 MHz
XXXIX ECPM

## Slide 3: K110 uses
Electronic components tests : Light/heavy ions
Track etched membranes: heavy ions
Material tests : light ions/ neutrons
University research
XXXIX ECPM

## Slide 4: Experimental hall
XXXIX ECPM

## Slide 5: Space radiations
Sources
  Solar Wind
  Cosmic rays
Composition
  Protons
  Heavy ions
  Electromagnetic radiations
XXXIX ECPM

## Slide 6: Beam requirements
Flux from few particles to 15000 ions/s.cm²
Homogeneity +/-10% on 25 mm
Range in Silicon larger than 60 µm
Different LET values available up to 60MeV/(mg/cm²) [Si]
Fast beam change : few minutes
XXXIX ECPM

## Slide 7: CRC cockails
XXXIX ECPM
M/Q=3,33 |  |  | 
Ion | Energy [MeV] | Range Si [µm] | LET Si [MeV/(mg/cm²)]
13C4+ | 131 | 269,3 | 1,3
22Ne7+ | 235 | 198,4 | 3,3
40Ar12+ | 370 | 117,1 | 10,2
58Ni17+ | 563 | 97,4 | 20,7
83Kr25+ | 750 | 91,8 | 32,6
M/Q=5 |  |  | 
Ion | Energy [MeV] | Range Si [µm] | LET Si [MeV/(mg/cm²)]
15N3+ | 60 | 57,8 | 3,3
20Ne4+ | 76 | 43,2 | 6,3
40Ar8+ | 146 | 38,5 | 15,5
84Kr17+ | 299 | 38,4 | 40,2
124Xe25+ | 417 | 36,4 | 69
124Xe35+ | 1000 | 73,1 | 62,5
High LET
High range

## Slide 8: Component cross section
XXXIX ECPM
Xe
Kr
Ni
Ar
Ne
N
C

## Slide 9: Development of a new ECRIS
Project funded by the Walloon region (Marshall plan : Skywin pole)
Objective : High charge state ion (Xe 35+ or 36+)
Increase the frequency : from 6 to 17,3 GHz
Room temperature coils
XXXIX ECPM

## Slide 10: Development of a new ECRIS
XXXIX ECPM
Source | Scampi | Blue Whale
Frequency | 6 GHz | 17,3 GHz
B ECR | 0,215 T | 0,618 T
B inj | 1,2 T | 2,0 T
B ext | 0,65 T | 1,25 T
B rad | 0,65 T | 1,25 T
Power consumption | ~100kW | ~100kW

## Slide 11: Development of a new ECRIS
XXXIX ECPM
Microwave Power : 2kW max
Plasma chamber
  diameter : 78 mm
  volume : 2,1 L
Coils current : 400 A
Available ions : C, N, Ne, Al, Ar, Ni, Kr, Xe
1m

## Slide 12: Hexapole configuration
XXXIX ECPM
Permanent magnet
9 rings
36 segments per ring
Higher coercivity for critical zones

## Slide 13: Development of a new ECRIS
XXXIX ECPM

## Slide 14: Xenon Spectrum
XXXIX ECPM
Gas : Xe and O2
Microwave power : 500W
Extraction voltage: 10 kV

## Slide 15: New cocktail
XXXIX ECPM
Ion | Energy on device | Range on device | LET on device
 | [MeV] | [µm] | [MeV/(mg/cm²)]
13C4+ | 131 | 269,3 | 1,3
14N4+ | 122 | 170,8 | 1,9
22Ne7+ | 238 | 202 | 3,3
40Ar12+ | 379 | 120,5 | 10,0
58Ni18+ | 582 | 100,5 | 20,4
84Kr25+ | 769 | 94,2 | 32,4
124Xe35+ | 995 | 73,1 | 62,5

## Slide 16: Special features for ions cocktail
Beam change in few minutes with only one operator : use of calibrated leaks
Decrease the beam intensity (100 fAe for N4+) : Use of pepper pot grid
XXXIX ECPM

## Slide 17: Heavy ions Irradiation Facility
XXXIX ECPM
90° bending magnet
Gold diffusion foil
Scanning magnet
beam monitoring detector
Irradiation Vacuum chamber

## Slide 18: Heavy ions Irradiation Facility
XXXIX ECPM
Faraday cup
Beam monitoring
Irradiation chamber

## Slide 19: Heavy ions Irradiation Facility
XXXIX ECPM

## Slide 20: Heavy ions Irradiation Facility
XXXIX ECPM
Calibration Pips
Scan Pips
Positioning camera

## Slide 21: Particles counting
Parallel Plate Avalanche Counter
  Transmission detector (Φ = 25 mm)
  In front of the vacuum chamber
  Surface normalization with a Pips before irradiation
  Count up to 15000 ions/s.cm²
XXXIX ECPM

## Slide 22: Beam homogeneity
Diffusion with a thin gold foil (0,75 µm)
  Energy loss
  Not adjustable
  Beam transport limitation
XXXIX ECPM

## Slide 23: Beam homogeneity
Scanning magnet
  Lissajoux figure
  Different frequencies for X and Y axes
Advantages
  Adjustable with the current
  No energy loss
XXXIX ECPM

## Slide 24: Lissajoux figure
XXXIX ECPM
Two triangle waves :
X : 13 Hz
Y : 50 Hz
Current up to 50 A
Power supply from JEMA

## Slide 25: Beam homogeneity
XXXIX ECPM

## Slide 26: SEU monitor
ESA reference component for quality control
Homogeneity and counting verification
Fast and visual test
XXXIX ECPM

## Slide 27: SEU monitor
XXXIX ECPM
20 X 20 mm
4 dies
128 memories by die
Procedure :
  Write
  Check
  Irradiate
  Read
  Number of error??

## Slide 28: Seu monitor
XXXIX ECPM

## Slide 29: Component cross section
XXXIX ECPM
Xe
Kr
Ni
Ar
Ne
N
C

## Slide 30
XXXIX ECPM
Thank you for your attention