## Slide 1: Particle Accelerators
A brief (hystorical) introduction
Reyes alemany fernandez (cern, BEAMS DEPARTMENT)

## Slide 2: Particle Accelerators
What for?
How can we observe such small particles?
Let’s try to build an accelerator

## Slide 3: What for?
30000 accelerators in use world-wide:
  44% radiotherapy
  41% ion implantation
  9% industrial applications
  4% low energy research
  1% medical isotope production
  <1% fundamental research

## Slide 4: The micro-world  the atoms
In a typical beach there are tens of thousands of millions of millions of sand grains
But … within a single grain of sand, there are as many atoms!

## Slide 5: The micro-world  atoms’ constituents
The atom nucleus weights more than 99% of the atom mass
If the atom was as big as the “Stade de France”
… the nucleus would be smaller than the foot ball

## Slide 6: How can we observe such small particles?
The structures under research are EXTRAORDINARILY SMALL (~ < 10-15 m)
probes with correspondingly high spatial resolution are needed. Visible light is inadequate: size ~ 5 10-7 m
what could we use instead?
mm = 10-3 m
µm = 10-6 m
nm = 10-9 m
pm = 10-12 m
fm = 10-15 m
am =10-18 m
light
 Ratoms ~ 30 – 300 pm (0.03 – 3 Å)
 Rnucleus ~ 1 – 10 fm
 Quarks - leptons

## Slide 7
How can we observe such small particles?
Aggregate of molecules: cell/bacteria
Size = 10-5 - 10-7 m
 10 micro – 100 nano
 0.1 eV – 10 eV
Optical microscope

## Slide 8
 | Size (m) | Size | Beam energy | Instrument
Aggregate of molecules: cell/bacteria | 10-5 | 10 micro meter | 0.1 eV | Optical microscope
 | 10-7 | 100 nano meter | 10 eV | 
Aggregate of atoms: molecules | 10-9 | 1 nano meter | 1 keV | Electron microscope
Atoms: nucleus+electrons | 10-10 | 0.1 nano meter | 10 keV | Synchrotron radiation
Nucleus (Oxygen: 8p+8n) | 10-14 | 0.01 pico meter | >100 MeV | Low energy e- or p+ accelerator
Aggregate of quarks: hadrons | 10-15 | 1 femto meter | > 1 GeV | High energy p+ accelerator
Quarks+leptons | 10-18 | 1 atto meter | > 1 TeV | High energy e- or p+ collider
How can we observe such small particles?
LHC 27 km circumference
7 TeV beam energy

## Slide 9: A little parenthesis about Energy Units
In physics, energy is usually measured in Joule (J)
Energy = capacity of a physical system to perform work
1 Joule = energy expended (or work done) in applying a force of one newton through a distance of one metre (SI).
Joule is not convenient when describing particle beams because the energy is very small, e.g.,
Energy = 1.602 10-19 J
Therefore a new unit was invented  eV  kinetic energy gained by a particle of elementary charge 1.602 10-19 C as it crosses a potential difference of 1 V.
1 keV = 103 eV, 1 MeV = 106 eV, 1 GeV = 109 eV, 1 TeV = 1012 eV

## Slide 10: How can we accelerate charged particles?
Simplest particle accelerators use a constant electric field (DC accelerators) between two electrodes, produced by a high energy voltage generator
One of the electrodes has the particle source
If e- beams: particle source is a thermionic cathode (widely used in vacuum technology)
In the accelerating region there is good vacuum to avoid beam-gas collisions
Exit window towards the target
Field-free field region
Depends on the maximum voltage that can be given by the generator
Limited achievable particle energies

## Slide 11: How can we accelerate charged particles?
CORONA FORMATION is the actual energy limit
-
HV
E
e- & ions acceleration
Cascade effect
What is the energy limit in DC accelerators?
electrode
Ionization of residual gas molecules in cascade
Spark discharge & HV breakdown
HV of ~ MV  particle energy ~ few MeV

## Slide 12: Examples of electrostatic accelerators
Cockroft-Walton (1030’s)
We had one at CERN to accelerate protons up to 750 keV
Van de Graaff (1030’s)
HV ~ 4 MV
HV ~ 2 MV – 10 MV

## Slide 13: How could we overcome the corona formation energy limit and go beyond few MeV regime?
Ising 1925  AC voltage!!
Wideroe 1928  first successful test of AC accelerator
vA
vB
LA
LB
vA < vB 
LB
> LA
 L = vTrf = βλo
-
+
+
-
E
E
RF generator voltage:
U(t)
Umax
Umin
Rolf Wideroe
Gustaf Ising

## Slide 14: AC Linear Accelerators
V
RF generator voltage:
Energy reached by the particle per crossed gap:
Eelectric is cte between s1 and s2 when the particle crosses the gap, therefore, q and Eelectric come out from the integral.
We are left with the integral of ds between s1 and s2  s2-s1 = Δs
= V
Average phase of the RF voltage the particle sees as it crosses the gap

## Slide 15: AC Linear Accelerators
Energy gained by the particle after passing the n-th gap:
Energy gain is proportional to the number of stages/gaps traversed by the particle
However, the largest voltage in the entire system is never greater than Umax
No corona discharge
At CERN we have linear accelerators for the first acceleration steps: LINAC2, LINAC3, LINAC4
Pulse of beam ~100 ms long every 1.2 s
DT (4 tanks,33 m)
750 keV
50 MeV

## Slide 16: What is the limitation of linear accelerators?
radiofrequency (RF) structures and a two-beam concept to produce accelerating fields as high as 100 MV per meter to reach a nominal total energy of 3 TeV
≈ 50 km
Size & cost could be a problem since it grows with energy

## Slide 17: How can we overcome the limitation of linear accelerators to increase the energy without increasing the size?
-
+
+
-
E
E

## Slide 18: How can we overcome the limitation of linear accelerators to increase the energy without increasing the size?
-
+
+
-
E
E

## Slide 19: How can we overcome the limitation of linear accelerators to increase the energy without increasing the size?
-
+
+
-
E
E

## Slide 20: But how can we keep a charged particle running in circles?
Let’s ask Lorentz

## Slide 21: But how can we keep a charged particle running in circles?
S
N
v
F
Curved trajectory!
We need a magnetic field
B
q: particle charge
Can we accelerate and bend neutral particles?
LORENTZ FORCE
If an electric field is present
If a magnetic field is present
Cross product of two vectors is another vector orthogonal to them
900
900

## Slide 22: Before we continue, first we should understand the beam rigidity
What is the condition for a circular orbit in the presence of a uniform magnetic field?
Lorentz force = centrifugal force
=
Beam rigidity formula
Mechanical equivalent
Lorentz force
B
ρ: curvature radius
m: particle mass
v: particle velocity
ρ
Particle momentum

## Slide 23: Let’s build our first circular accelerator!!
We need a magnetic field perpendicular to the particle trajectory to bend the particles
We need an electric field to give energy to the particles  magnetic fields do not change the energy of the particles, why?
Those are vectors! They have direction and magnitude
This is the scalar product:
If A and B are parallel  θ = 00  cosθ = 1
The force gives the maximum energy increase
If A and B are orthogonal  θ = 90o  cosθ = 0
= 0
Since the magnetic field is orthogonal to the particle trajectory = 0

## Slide 24: This is our first circular accelerator  cyclotron
B ~ 2 T
The first circular accelerator was developed by E. O. Lawrence at Univ. California in 1930.
In 1932 Lawrence and Livingston built the first cyclotron suitable for experiments with 1.2 MeV peak energy.
If B is a constant uniform magnetic field  ρ increases as the particle momentum increases
E. O. Lawrence
The vacuum chamber has to be big enough to accommodate the full particle trajectory before extraction
Vacuum chamber

## Slide 25: A little parenthesis about Relativity
For over 200 years Newton’s equations of motion were believed to describe nature correctly. But in 1905 Einstein discovered an error in these laws and proposed a solution.
Newton assumes m is constant
But Einstein, based on experimental observations, realised that the mass of a body increases with velocity!!
m0 is the rest mass, the mass of a not-moving body
c: speed of light (3x105 km/s)

## Slide 26: A little parenthesis about Relativity
Relativistic gamma factor
As the velocity of the particle gets closer to c, the mass m is greater and greater
The body inertia increases and increases and the force applied to move the particle is less and less efficient, so the velocity increases more and more slowly and asymptotically approaches c
But it will never be equal to c because the mass grows exponentially
v/c
LHC protons
Relativistic beta factor
e.g. LHC

## Slide 27: We are doing well so far, but MeV it is not enough, how can we reach GeV energies?
 | Size (m) | Size | Beam energy | Instrument
Aggregate of molecules: cell/bacteria | 10-5 | 10 micro meter | 0.1 eV | Optical microscope
 | 10-7 | 100 nano meter | 10 eV | 
Aggregate of atoms: molecules | 10-9 | 1 nano meter | 1 keV | Electron microscope
Atoms: nucleus+electrons | 10-10 | 0.1 nano meter | 10 keV | Synchrotron radiation
Nucleus (Oxygen: 8p+8n) | 10-14 | 0.01 pico meter | >100 MeV | Low energy e- or p+ accelerator
Aggregate of quarks: hadrons | 10-15 | 1 femto meter | > 1 GeV | High energy p+ accelerator
Quarks+leptons | 10-18 | 1 atto meter | > 1 TeV | High energy e- or p+ collider

## Slide 28: What is the limitation of the cyclotrons?
If B is a constant uniform magnetic field  ρ increases as the particle momentum increases  we get a spiral orbit  cyclotron
But there is a limitation to the B field
In the end the spiral gets bigger and bigger
 the size (= cost) of the cyclotron has to increase!

## Slide 29: What can we do to keep the radius of the accelerator cte?
If B increases synchronously with the particle momentum such the ratio p/B remains cte, then the accelerator radius is cte.
There is a technical limit to the value of B, ~ 1.5 Tesla for normal conducting magnets and ~ 8 Tesla for superconducting magnets
Synchrotrons
E. M. McMillan
V. Veksler
Synchrotron principle developed almost simultaneously by E. M. McMillan (California University) & V. Veksler (Soviet Union) in 1945.
1949: Cosmotron @BNL  proton synchrotron of 3.3 GeV, C ~ 57 m
2008: LHC  proton synchrotron of 7000 GeV, C = 27 km

## Slide 30: Let’s build a synchrotron

## Slide 31: We need dipole magnets
A dipole with a uniform field deviates a particle by an angle θ
The bending angle θ depends on:
  the length L
  the magnetic field B
  the particle momentum
S
N
v
F
Curved trajectory!
B
900
900
L
Dipole seen from the top

## Slide 32: Two particles in a dipole field
Particle A
Particle B
Lets unfold these circles……
What happens with two particles that travel in a dipole field with different initial angles, but with equal initial position and equal momentum ?
Assume that Bρ is the same for both particles.

## Slide 33: The 2 trajectories unfolded
This type of oscillation forms the basis of all transverse motion in an accelerator.
It is called Betatron Oscillation
The horizontal displacement of particle B with respect to particle A.
Particle B
Particle A
2π
0
displacement
Strength of the dipole field normalized to the particle momentum/charge:
Particle B oscillates around particle A  a dipole magnet bends the particle in the horizontal plane and has a focusing effect proportional to 1/ρ (1/bending radius)
Remember, this is the horizontal plane
x
L
Remember two slides ago:

## Slide 34: What happens in the vertical plane?
Particle B
Particle A
2π
0
displacement
y
α
L
y = αL
Vacuum pipe aperture
Particle is lost
What can we do to keep the particle inside the vacuum pipe?
We need something that when the particle deviates from the reference trajectory by an amount y, there is a force applied to the particle proportional to y that brings the particle back on track
Do you know a force of this kind?

## Slide 35: The mechanical equivalent
The gutter below illustrates how the particles in our accelerator should be focused
The force we are looking for is of the type:

## Slide 36
A particle during its transverse motion in our accelerator is characterized by:
  Position or displacement from the central orbit
  Angle with respect to the central orbit
x = displacement
x’ = angle = dx/ds
This is a motion with a linear restoring force =f(position), like the pendulum or spring mass system
ds
x’
x
dx
x
s
x’
x

## Slide 37: Quadrupole fields
Normalised gradient, k:
On the x-axis (horizontal) the field is vertical and given by
By ∝ x
On the y-axis (vertical) the field is horizontal and given by
Bx ∝ y
Field gradient, K:
A Quadrupole has 4 poles, 2 north and 2 south
There is no magnetic field along the central axis
They are symmetrically arranged around the centre of the magnet
Magnetic field
x
y
Magnetic field
x
y
Horizontal focusing quadrupole
Vertical focusing quadrupole
Hook’s law

## Slide 38: Focusing and Stable motion
Using a combination of focusing (QF) and defocusing (QD) quadrupoles solves our problem of ‘unstable’ vertical motion.
Remember that the focusing strength of a dipole magnet goes with
The bigger the accelerator radius, ρ, the smaller the strength of the dipole field
So the focusing effect in the horizontal plane works for small radius accelerators, but would it work for LHC?
Even for smaller radius accelerators would not work
Does not matter!! We’ll profit from the focusing effect of the quadrupoles because it works in both planes!!!!

## Slide 39
COSMOTRON (1949) & BEVATRON (1954) used weak focusing (strong focusing not yet invented)  beam area in BEVATRON ~ 120 cm2  huge vacuum chambers
Beam direction
Vacuum chamber

## Slide 40: Focusing and Stable motion
Quadrupoles will keep the beams focused in both planes when the position in the accelerator, type and strength of the quadrupoles are well chosen
By now our accelerator is composed of:
  Dipoles, constrain the beam to some closed path (orbit)
  Focusing and Defocusing Quadrupoles, provide horizontal and vertical focusing in order to constrain the beam in transverse directions
A combination of focusing and defocusing sections that is very often used is the so called: FODO lattice
This is a configuration of magnets where focusing and defocusing magnets alternate and are separated by non-focusing drift spaces

## Slide 41: FODO cell
The FODO cell is defined as follows:
Focusing quadrupole (QF) focuses in horizontal and defocuses in vertical
Magnetic field
x
y
Beam
Magnetic field
x
y
Defocusing quadrupole (QD) focuses in vertical and defocuses in horizontal
‘FODO’ cell
QF
QD
QF
L2
L1

## Slide 42: Circular accelerator with a FODO structure
(by K. Wille)
(by K. Wille)

## Slide 43: What do we know by now?
We know how to guide the particles on a well defined design orbit
We know how to focus the particles to keep each single particle trajectory with in the vacuum chamber of the accelerator close to the design orbit
In this way particles are accelerated and stored for several hours (~ 12 hours or more) travelling at about v~c  L= 1010-1011 km several times the distance Sun-Pluto and back
LHC vacuum pipe Ultra high vacuum: 10-10 mbar, like at 1000 km over see level
Diameter ~ 4-5 cm

## Slide 44: At which energy can we accelerate the particles now? Let’s take LHC as example
~ 66% of the lattice elements are dipoles
Circumference  FIXED!!! by LEP: 26658.9 m 
7 TeV
Field limit for normal conducting magnets due to saturation
We need SUPERCONDUCTING technology!!
Golden formula (you should know by heart) 
Magnetic field in the dipole magnets = 8 Tesla
 | Size (m) | Size | Beam energy | Instrument
Aggregate of molecules: cell/bacteria | 10-5 | 10 micro meter | 0.1 eV | Optical microscope
 | 10-7 | 100 nano meter | 10 eV | 
Aggregate of atoms: molecules | 10-9 | 1 nano meter | 1 keV | Electron microscope
Atoms: nucleus+electrons | 10-10 | 0.1 nano meter | 10 keV | Synchrotron radiation
Nucleus (Oxygen: 8p+8n) | 10-14 | 0.01 pico meter | >100 MeV | Low energy e- or p+ accelerator
Aggregate of quarks: hadrons | 10-15 | 1 femto meter | > 1 GeV | High energy p+ accelerator
Quarks+leptons | 10-18 | 1 atto meter | > 1 TeV | High energy e- or p+ collider
Finally we can observe quarks and leptons!!
WELL DONE !!!

## Slide 45: Spares

## Slide 46: Hill’s equation
These betatron oscillations exist in both horizontal and vertical planes.
The number of betatron oscillations per turn is called the betatron tune and is defined as Qx and Qy.
Harmonic oscillator equation of motion:
If the restoring force, K is constant in ‘s’ then this is just a Simple Harmonic Motion.
Newton’s second law
Hooke’s law

K
In a real accelerator K = f(s), remember the FODO, there are different quadrupole magnets, each can have its own value for the restoring force.
The equation of motion is in this case
Hill’s equation, with K(s):
Focusing effect: from dipoles from quadrupoles

## Slide 47: This is our first circular accelerator  cyclotron
Equation of motion within the homogeneous magnetic field:
It is the Lorentz force without the electric field:
The particle follows a circular orbit with revolution frequency:
Cyclotron frequency
The higher the velocity the larger the radius of curvature (provided the mass remains cte)  the particle gets more and more “rigid” and the magnetic field, which remains constant, has more and more difficulties to bend the particle.
The RF frequency = cyclotron frequency
Not valid for relativistic particles
f(particle velocity)

## Slide 48: This is our first circular accelerator  (synchro)cyclotron
Classical cyclotrons can accelerate protons, deuterons and alpha particles up to 22 MeV per charge.
At this energies those particles are not relativistic ( v ~ 0.15c), so the mass ~ cte, so the cyclotron frequency remains cte.
As the energy increases the particles are more and more relativistic and their mass is not cte, it increases:
Therefore, ωz decreases with increasing m
If ωRF is decreased accordingly, higher energies can be reached.
This is the synchrocyclotron principle

## Slide 49: How can we observe such small particles?
Let’s ask De Broglie
In his 1924 PhD thesis suggested that
“MOVING OBJECTS ACT LIKE WAVES”
A particle of mass m and speed v behaves like a wave with wavelength λ:

## Slide 50: How can we observe such small particles?
De Broglie wavelength
We just saw that photons are limited in size, what else we can use?
Good candidates are the microscopic particles itself
We just learnt they are waves as well
Its De Broglie wavelength must be small compared to the size of the structure we want to observe

## Slide 51
How can we observe such small particles?
Aggregate of atoms: molecules
Size = 10-9 m  1 nano
 1 keV
Electron microscope
This is an accelerator!!

## Slide 52
How can we observe such small particles?
Atoms: nucleus+electrons
Size = 10-10 m  0.1 nano
 10 keV
Synchrotron radiation facility