## Slide 1: Colliders and The Large Hadron Collider I. LHC layout II. LHC Operational cycle III. Beam measurements
[R. Alemany]
[CERN BE/OP]
Lectures UCLouvain (30.03.2022)

## Slide 2: Why colliders?
What is the centre of mass energy  the interesting energy because it is the only one available for the collision products  when two particles of masses m1 and m2 collide?
Four-momentum
Square of the four-momentum:
CASE 1:
(m1,p1)
(m2,0)
CASE 2:
(m1,p1)
(m2,-p1)

## Slide 3: Why colliders?
CASE 1:
To get a Ecm = 630 GeV to do a SppS collider (SPS in the 80’s discovered the weak neutral currents with this collider), what should be the value of E1,lab?
E1,lab ~ 212 TeV
To get a Ecm = 14 TeV to do an LHC collider (LHC discovered the Higgs in 2012) what should be the value of E1,lab?
E1,lab ~ 100 PeV
If colliders would not have been invented we would not have discovered yet many particles
First collider

## Slide 4: Why colliders?
From the point of view of the energy, a collider is very very interesting
However it has some disadvantages:
The beam is several orders of magnitude less dense than a fixed target  less number of interactions per second
  How do we overcome this issue?
We collide for many hours  e.g. LHC collisions ~ 12 – 15 hours
2. The collision products go out in all directions  experiment has to cover all the space around the beam pipe
  Experiments located around the beam pipe are difficult to take in/out to install a new experiment.
  Fixed target experiments are more flexible, e.g. SPS north area: tens of experiments per year.

## Slide 5: I. Basic layout of the machine
SPS (~7 km)
LHC (27 km)
IR4
IT
ARC
MS
DS
Sector 34
Beam Dump System
Betatron cleaning collimators
Momentum cleaning collimators
IP1
IP2
IR3
IP5
IR6
IR7
IP8

## Slide 6: I. Basic layout of the machine: the arc
MB: main dipole
MQ: main quadrupole
MQT: Trim quadrupole
MQS: Skew trim quadrupole
MO: Lattice octupole (Landau damping)
MSCB: Skew sextupole +
Orbit corrector (lattice chroma+orbit)
MCS: Spool piece sextupole
MCDO: Spool piece octupole +
Decapole
BPM: Beam position monitor
LHC TDR
LHC arc cells = FoDo lattice* with
~ 90º phase advance per cell in the V & H plane
F
o
D
o
B1
F
D
B2

## Slide 7: I. Basic layout of the machine
~ 66% of the lattice elements are dipoles
Circumference  FIXED!!! by LEP
FIXED, no choice
p = nucleon momentum  defined by the physics case  TeV range  7 TeV
Field limit for normal conducting magnets due to saturation
We need SUPERCONDUCTING technology
Golden formula (you should know by heart)

## Slide 8: I. Basic layout of the machine: Superconducting magnets
Superconducting cables of Nb-Ti
LHC ~ 27 km circumf. with 20 km of superconducting magnets operating @8.3 T. An equivalent machine with normal conducting magnets would have a circumference of 100 km and would consume 1000 MW of power  we would need a dedicated nuclear power station for such a machine. LHC consumes ~ 10% nuclear power station
1 mm
6 µm Ni-Ti filaments
Total amount of He used @LHC ~500-700 T
He gas  liquid @ 4.2 K  superfluid @ 2.17 K
λ point

## Slide 9: I. Basic layout of the machine: main cryodipoles (two dipoles in one)
The geometry of the main dipoles
(Total of 1232 cryodipoles)
Superconducting coils
  Beam pipe (Ultrahigh beam vacuum 10-10 Torr like at 1000 km over see level)
L ~ 15 m
8.3 T, 11.87 kA
T = 1.9 K, ~27.5 ton
Iron yoke
Collars
He Vessel
Vacuum vessel (10-6 mbar)
Thermal shield
Heat
exchanger
Beam Screen
(Stainless Steel
+ Cu)
Cold bore non-magnetic austenitic steel
46.5 mm
36.9 mm

## Slide 10: I. Basic layout of the machine: main quadrupoles
Integrated gradient = 690 T
Nominal gradient = 223 T/m
Inominal = 11.87 kA
L=3.1 m
194 mm (cold)
56 mm (warm)
55 per sector

## Slide 11: I. Basic layout of the machine: main dipoles Field quality
The magnetic field of the main dipoles:
The stability of the geometry of the superconducting
coils is essential to the field quality.
Mechanical stress during coil assembly
Thermal stresses during cool-down
Electromagnetic stresses during operation
Additional sources of field errors are the dimensional tolerances of the magnet components and of the manufacturing and assembling tooling.
The relative variations of the integrated field and of the field shape imperfections must not exceed ~ 10 -4 and
= sources of deformations of the coil geometry
tough
Reference: LHC Project Report 501
“Field Quality Specification for the LHC Main Dipole Magnets”

## Slide 12: I. Basic layout of the machine: main dipoles Field quality
Why the tolerances are so tight?
 Because the field quality determines how long the particles can circulate in the accelerator
Up to which order do we care?
 Up to n = 7 at least
~ 10-4

## Slide 13: I. Basic layout of the machine: main dipoles Field quality
Error | Side effects if error is > few 10-4 | Corrected with
a1 | Closed orbit perturbations and thus feed-down contributions from higher order multiple errors | Dipole correctors (MCB)
b1 |  | 
a2 | Linear coupling and vertical dispersion | Skew quadrupoles (MQS)
b2 | Tune change, β and dispersion beating | Trim quadrupoles (MQT)
a3 | Chromatic coupling and Q’’ | Skew sextupoles (MSS)
b3 | b2 feed-down at injection (persistent current effect) and off-momentum β-beat | Sextupole (MCS)
a4 | Dynamic aperture (DA) at injection | 
b4 | DA and Q’’ at injection | Octupole (MCO)
a5 | DA for off-momentum particles at injection | 
b5 | DA and Q’’’ at injection | Decapole (MCD)
a6 to b7 | DA at injection | 
Sextupole
Sextupole+octupole

## Slide 14: I. Basic layout of the machine: dipole corrector magnets
LHC TDR
F
o
D
o
MCS
Nominal main field strength = 1630 T/m2
Inominal = 550 A, 1.9 K, L=15.5 cm, ~10 kg
5.8 cm
MCD:
Nominal main field strength ~ 120 T/m4
Inominal = 550 A, 1.9 K, L=11 cm, ~6 kg
MCO:
Nominal main field strength = 8200 T/m3
Inominal = 100 A, 1.9 K, L=11 cm, ~6 kg
MCDO

## Slide 15: I. Basic layout of the machine: quadrupole corrector magnets
LHC TDR
F
o
D
o
MQT/MQS
MQT/MQS:
Nominal main field strength = 123 T/m
Inominal = 550 A, 1.9 K L=38 cm, ~250 kg
MO:
Nominal main field strength = 63100 T/m3
Inominal = 550 A, 1.9 K L=38 cm, ~8 kg
MSCB
MCBM (dipole):
Nominal main field strength = 2.93 T
Inominal = 55 A, 1.9 K, L=78.5 cm, ~143 kg
MSM (sextupole):
Nominal main field strength = 4430 T/m2
Inominal = 550 A, 1.9 K, L=45.5 cm, ~83 kg
MO
Chromaticity
Orbit
Landau damping
MQT: Trim quadrupole
MQS: Skew trim quadrupole

## Slide 16: I. Basic layout of the machine: quadrupole corrector magnets
(Courtesy of B. Holzer)
LHC TDR
F
o
D
o
Why the orbit and sextupole correctors are placed close to a quadrupole?

## Slide 17: I. Basic layout of the machine: quadrupole corrector magnets
QF
β (m)
D (m)
Magnet strength
(Natural chromaticity term)
Chromaticity correction terms

## Slide 18: I. Basic layout of the machine
SPS (~7 km)
LHC (27 km)
IR4
IT
ARC
MS
DS
Sector 34
Beam Dump System
Betatron cleaning collimators
Momentum cleaning collimators
IP1
IP2
IR3
IP5
IR6
IR7
IP8

## Slide 19: I. Basic layout of the machine: Dispersion suppression
Cancels the horizontal dispersion generated on one side by the arc dipoles and on the other by the separation/recombination dipoles and the crossing angle bumps
Helps in matching the insertion optics to the periodic solution of the arc
If only dipoles are used they cannot fully cancel the dispersion, just by a factor 2.5. Therefore individual powered quadrupoles are required (Q8-Q11 with I ~ 6000 A)
Q11
Q10
Q9
Q8
MBARC
DS
LSS
ARC
empty
The schema applies to all DS except the ones in IR3 and IR7
(Courtesy of B. Holzer)

## Slide 20
Direction IP5
Dispersion (m)
2 m
I. Basic layout of the machine: Dispersion suppression
Why do we suppress dispersion before reaching the IP?
DISPERSION SUPPRESION
ARC
Beam size here?
When you design your beam pipe you have to take into account the contribution of D(s)
0 m
D(s) is created by the dipole magnets and afterwards focused by the quadrupoles
The inhomogeneous solution changes the beam size …

## Slide 21: I. Basic layout of the machine
SPS (~7 km)
LHC (27 km)
IR4
IT
ARC
MS
DS
Sector 34
Beam Dump System
Betatron cleaning collimators
Momentum cleaning collimators
IP1
IP2
IR3
IP5
IR6
IR7
IP8

## Slide 22: I. Basic layout of the machine: Luminosity insertions
Q2
Q1
Q3
IP1
TAS*
Q1 Q2 Q3
D1
(1.38 T)
TAN*
D2 Q4
(3.8 T)
Q5
Q6
Q7
4.5 K
1.9 K
Warm
Separation/ Recombination
Matching Quadrupoles
Inner Triplet
1.9 K
ATLAS
R1
* Protect Inner Triplet (TAS) and D2 (TAN) from particles coming from the IP
4.5 K
4.5 K
188 mm
Tertiary collimators
6.45 kA
10.63 kA
23.85
18.95
22.5
17.6
29.0
24.0
To provide sufficient aperture for the Xangle
The mechanical aperture of the inner triplets limits the maximum * @IPs and the maximum Xangle  limit peak lumi
DS

## Slide 23: Luminosity
Two figures of merit in a collider: energy and luminosity
Luminosity = number of interactions per unit of time
cross-section at the given energy of the interested physics
l
h
w
l
h
w
t
with I = q/t
Number of particles of the first beam in the cube:
The orange beam is crossed by n2 particles per unit of time:
I/s=intensity per cm2

## Slide 24: Luminosity
The number of events per unit of time for two beams of 1 cm2 is:
and for beams of a general area s = wh
If we replace q = 1.6e-19 coulomb and c = 3e10 cm/s:

## Slide 25: Luminosity for bunched beams
Reference:
For two bunches colliding HEAD ON with Gaussian beam density distribution and equal beam sizes:
Ni: number of particles in one bunch
f: revolution frequency
Nb: number of bunches in one beam
sigma: beam size

## Slide 26: Luminosity for bunched beams
Examples:

## Slide 27
~ 65 fb-1
2018
LHC Integrated performance

## Slide 28: I. Basic layout of the machine: Luminosity insertions
IP
D1
D2
Q1
Q2
Q3
Q3
Q2
Q1
D1
D2

## Slide 29: I. Basic layout of the machine: Luminosity insertions
With nominal LHC parameters:
2808 bunches separated 25 ns
We can have up to 30 parasitic interactions around the IP
IP
D1
D2
Q1
Q2
Q3
Q3
Q2
Q1
D1
D2

## Slide 30: I. Basic layout of the machine: Luminosity insertions
IP
D1
D2
Q1
Q2
Q3
Q3
Q2
Q1
D1
D2
Crossing angle reduces the luminosity

## Slide 31: I. Basic layout of the machine: Luminosity insertions
Beam-beam separation
Beam-beam separation = f(σ)
Aperture limitation = f(σ, beam pipe size)
β is very small at the IP, but very big at the Inner triplets 
Therefore, the quadrupoles around the IP have such a big apertures
IP
D1
D2
Q1
Q2
Q3
Q3
Q2
Q1
D1
D2
Aperture limitation
Crossing angle (e.g. 285 µrad )

## Slide 32: I. Basic layout of the machine: High luminosity insertions
ATLAS
five-storey building
CMS

## Slide 33
RB.A12
RQ6.L1
Current (A)
Time
RAMPDOWN
INJECTION PROBE
INJECTION PHYSICS
PREPARE RAMP
RAMP
FLATOP
SQUEEZE
ADJUST
STABLE BEAMS…
SETUP
II. LHC Operational cycle
~ 2 hours
10 to 15 hours
Exp-LHC

## Slide 34: II. LHC Operational cycle: Squeeze  reduce β*
So even tough we squeeze our N1,2=100,000 million protons per bunch down to 16 microns (1/5 the width of a human hair) at the interaction point. We get only around 20 collisions per crossing with nominal beam currents.
The bunches cross (every 25 ns) so often we end up with around 600 million collisions per second - at the start of a fill with nominal current.
Most protons miss each other and carry on around the ring. The beams are kept circulating for hours  10 hours
Squeeze the beam size down as much as possible at the collision point to increase the chances of a collision

## Slide 35: II. LHC Operational cycle: Squeeze  reduce β* (β @IP)
Remember: there is no D(s) here
β=4500 m
(@450 GeV)~480
εn=3.5 µm rad
σ ~ 6 mm !!
IR2
IR1
IR3
IR4
IR5
IR6
IR7
IR8
IR1
Beta function at top energy and after squeeze
4500 m
Beta function at Injection
IR1
IR5
IR1
IR3
IR4
IR6
IR7
IR8
IR2
250 m
180 m
180 m
@ 7 TeV
σIT ~ 1.2 mm
@IP β*=0.5 m
Rbeampipe~29/24 mm
we could only accommodate ~ 4 times the beam size and we need at least 7σ clearance
Inner Triplets
Why we cannot have β*= 0.5 m at injection?

## Slide 36: II. Beam measurements: Beam trajectory
Each point is a BPM (Beam Position Measurement)
49 mm aperture
ARC BPMs
Betatron oscillation
A
B
beam
TA
TB
If you count the number of betatron oscillations,
which beam parameter do you get?

## Slide 37: II. Beam measurements: Beam trajectory correction
MSCB
Chromaticity
Orbit
MSM (sextupole)
MCBM (dipole)
LHC TDR
F
o
D
o
Why the orbit and sextupole correctors are placed close to a quadrupole?

## Slide 38: II. Beam profile measurements: Beam 1 on TDI screen – 1st and 2nd turns
ALICE
Scintillator screen for LBDS

## Slide 39: II. Beam profile measurements: Emittance measurement - Wire scanner
Emittance is the figure of merit for profile measurements.
But it is a derived quantity from the beam size ()

  = 2/β
Which we measured before
Where would you install a wire scanner in LHC to get the beam size and then the emittance?
Courtesy of A. Guerrero

## Slide 40: II. Beam measurements: Aperture scan
BLM*
*Beam Loss Monitor = Ionization chamber

## Slide 41: II. Beam measurements: Dispersion measurement
RF
IR3
OFF-MOMENTUM particles cleaning system
Horizontal Dispersion (m)
Vertical Dispersion (m)
D(s) = 0 m

## Slide 42: II. Beam measurements: Beta measurement
Courtesy of B. Holzer (lectures)
1st Change quadrupole strength in steps
2nd Measure Tune
3rd Plot Tune vs Quadrupole strength
kL
Qx,Qy

## Slide 43: II. Beam measurements: Fast BCT (Beam Current Transformer)
FBCT
beam
Intensity
~ 3 109
Each point is a bunch
Total number of bunches = 1380
B1
B2

## Slide 44: Spare slides

## Slide 45
production rate of events is determined by the cross section Σreact
and a parameter L that is given by the design of the accelerator:
… the luminosity
remember:
1b=10-24 cm2
Official number: 1400 clearly identified Higgs particles “on-tape”
Integrated luminosity during RUN I
41/42
High Light of the LHC

## Slide 46
ATLAS event display: Higgs => two electrons & two muons
42/42
High Light of the HEP year

## Slide 47: I. Basic layout of the machine: Superconducting magnets
Superfluid helium  Why is it so great?!!
  very high thermal conductivity is able to conduct away heat a thousand times better than a metallic conductor like copper
  very low viscosity coefficient  can penetrate tiny cracks, deep inside the magnet coils to absorb any generated heat
  very high heat capacity  prevents small transient temperature fluctuations

## Slide 48: XIV. Beam captured – mountain range display
Now RF ON
Bunch length ~ 1.5 ns  ~ 45 cm
Turn number

## Slide 49: Beam parameters (nominal)
 |  | Injection | Collision | 2012
Proton energy | GeV | 450 | 7000 | 4000
Particles/bunch |  | 1.15 x 1011 |  | 1.6 x 1011
Num. bunches |  | 2808 |  | 1380
Longitudinal emittance (4) | eVs | 1.0 | 2.5 | 
Transverse normalized emittance | µm rad | 3.5 | 3.75 | 
Beam current | A | 0.582 |  | 
Stored energy/beam | MJ | 23.3 | 362 | 
Peak luminosity related data |  |  |  | 
RMS bunch length | cm | 11.24 | 7.55 | 
RMS beam size @IP1 & IP5  x,y =  | µm | 375.2 | 16.7 | 
RMS beam size @IP2 & IP8  x,y =  | µm | 279.6 | 70.9 | 
Geometric luminosity reduction factor (F) |  |  | 0.836 | 
Instantaneous lumi @IP1 & IP5 (IP2Pb-Pb, IP8) | cm-2s-1 |  | 1034(1027 , 1032) | 7 1033
Instantaneous lumi/bunch crossing @IP1 & IP5 | cm-2s-1 |  | 3.56 x 1030 | 
* = 0.55 m
 = 0.5 nm rad
* = 0.6 m
n = 2.5 µm rad

## Slide 50: pPb physics during 2013
5 kHz difference at injection
+ 250 μm
p+
- 250 μm
Pb82+208
On momentum orbit
Off momentum orbit

## Slide 53: I. Basic layout of the machine: main cryodipoles (two dipoles in one)
The geometry of the main dipoles
(Total of 1232 cryodipoles)
Length of the bend part =14.3 m
Distance between apertures = 194.5 mm
ρ = 2.8 km
(R = 4.3 km)
The active part of the cold mass is bent in the horizontal plane with an angle of 5.09 mrad with ρ = 2.8 km. The shape of the two beam channels is identical.
HORIZONTAL PLANE
The theoretical shape of the beam channels is a straight line, while the natural shape has ~ 0.3 mm deflection between two supports at 5.4 m distance
VERTICAL PLANE
L ~ 15 m
8.3 T, 11.87 kA
T = 1.9 K, ~27.5 ton
What is the maximum energy a proton can reach?
What is the maximum energy a 208Pb82+ can reach?

## Slide 54: II. The experiments: Low luminosity insertions: LHCb
Centre of the exp cavern

## Slide 55: IV. Momentum and betatron cleaning insertions (IR3, IR7)
14
50
6(9)
Settings @7TeV and *=0.55 m
Beam size () = 300 µm (@arc)
Beam size () = 17 µm (@IR1, IR5)
7
8.5

## Slide 56: I. Basic layout of the machine: quadrupole corrector magnets

## Slide 57: II. LHC Operational cycle: Squeeze  reduce β*
ATLAS=CMS
Q1
Q3
D2
Q5
Q2
D1
Q4
Q6
Q7
2MB
Q8
2MB
Q9
2MB
Q10
2MB
Q11
IT
MS
DS
Remember what I said in slide 23  The mechanical aperture of the inner triplets limits the maximum * @IPs and the maximum Xangle  limit peak luminosity

## Slide 58: II. Beam measurements: Integer tunes
Qx = 64
Qy = 59

## Slide 59: I. Basic layout of the machine: Dispersion suppression
Quadrupole types: MQ, MQM, MQTL
Nominal gradient = 200/160 T/m
Inominal = 5.4/4.3 kA
Lmag=2.4/3.4/4.8 m
T=1.9/4.5 K
Cold bore = 53/50 mm
Individual powered apertures
MQM
5 m
18/42

## Slide 60: I. Basic layout of the machine: Low luminosity insertions
LHCb
Q7
Q6
Q5
Q4
D2
MKI
Q1 Q2 Q3
ALICE
IP8
LHCb
MSI
TDI
TCDD
D1
Beam 1
Beam 2
Beam 2
Beam 1
Extra challenge  the lattice has to accommodate the injection region
26/42

## Slide 61: I. Basic layout of the machine
46.5 mm
36.9 mm
LHC TDR
LHC arc cells = FoDo lattice* with
~ 90º phase advance per cell in the V & H plane
F
o
D
o
Why ~ 90º phase advance per cell is a good number?
σinjβ ~1 mm
7-10σ
Which parameter determines the beam size (ignoring D(s))?
(In general in proton machines εx≈εy  beams are round)
In order to get the maximum aperture possible the β(s) in both planes have to be minimized:
27/42

## Slide 62: II. Beam measurements: Beta measurement
Reference: Record low beta beating in the LHC
Tomas, R. et al. Phy. Rev. Special Topics - Accelerators and Beams15(9).
Achieved β-beating error 10% !!
Why is so important to have a small uncertainty in the beta function?
38/42

## Slide 63: II. Beam measurements: Non-integer tunes
BPM pos  FFT  tune
Qx·frev = 3 kHz
A
B
beam
TA
TB
With a frequency of ~3 kHz we measure the same beam position
FODO: Ψ=180o
BPM
F/2
D
F/2
Every 2xT we measure the same position:
Qx = .279
Qy = .310
@LHC
39/42