## Slide 1
Design of a new amorphous Silicon-based
Flat Panel Detector for Particle Therapy
1Khalil El Achi, 1Eduardo Cortina Gil,
2Alexis Warnier, 2Victor De Beco, 2Severine Rossomme
1Université Catholique de Louvain, Louvain-la-Neuve, Belgium
2IBA Dosimetry, Louvain-la-Neuve, Belgium

## Slide 2
Proton Stopping Power
The energy loss of different particles is characterized by the Bethe-Bloch equation,
The energy loss depends on the initial energy of the particle beam and the density of the medium.
Proton’s stopping power increases as the particle slows down and maximizes at the end of the trajectory.
This special behavior is exploited to treat chronic cancers and tumors that are difficult to treat with surgical and pharmaceutical procedures [1].
[1] Durante, M., Orecchia, R., & Loeffler, J. S. (2017). Charged-particle therapy in cancer: clinical uses and future perspectives. Nature Reviews Clinical Oncology, 14(8), 483-495.

## Slide 3
Proton Therapy (PT) and Conventional Radiotherapy (RT)
Proton therapy:
  Utilizing highly accelerated protons of range 60 – 250 MeV
  Particles penetrate the tissue and deposit the lethal dose to a small region
  Preserving healthy cells located around the tumor
Conventional Radiotherapy
  Ɣ-rays of energy range 6 – 25 MeV
  Most common form of radiation treatment
  Dose delivered around the tumor
  Significant non-lethal dose delivered all around the tumor [2]
[2] E. C. Halperin, “Particle therapy and treatment of cancer,” The lancet oncology, vol. 7, no. 8, pp. 676–685, 2006.

## Slide 4
Tumor
Healthy cells receiving a non-lethal dose
Spread Out Bragg Peak (SOBP)
By superpositioning the different segmented Bragg peaks concerning energy and dose, a consistent dose can be delivered to the tumor region.
By setting the minimum and maximum energy needed, depending on the penetration depth
Where the range of protons in water follows the close power-law relationship:
Where R is the range in water, E is the energy of the proton beam, , and [3].
[3] Jette, D., & Chen, W. (2011). Creating a spread-out Bragg peak in proton beams. Physics in Medicine & Biology, 56(11), N131.

## Slide 5
Proton
Beam
Patient
Tumor
The pencil beam traced the irradiated area layer by layer
Proton therapy delivery techniques – Pencil Beam Scanning (PBS)
Scanning Magnets
X- direction
Y- direction
The modern proton therapy delivery technique, where the proton beam is magnified and steered by a set of magnets.
Has the capacity for Ultra-High-Dose Rate (UHDR) proton FLASH therapy [4]
[4] B. Lin, D. Huang, F. Gao, et al., “Mechanisms of flash effect,” Frontiers in Oncology, vol. 12, p. 995 612, 2022.

## Slide 6
70 MeV Spot
220 MeV Spot
X-position (mm)
Proton Pencil Beam Scanning Dose Distribution
Proton therapy delivery techniques – Pencil Beam Scanning (PBS)
The beam delivers the dose to a magnified spot depending on the energy of the beam
The beam spot has a Gaussian profile with:
*Simulated with Geant4
*acquired by IBA Sphinx Compact Detector

## Slide 7
Patient-Specific Quality Assurance (PSQA) - Ionization Chambers
PBS flat field scanning
Detector Placement
water
To accurately deliver the dose, quality assurance practices have to be done
Medical Dosimetry:
  Irradiating a particle detector with the treatment plan, to verify the delivered dose

## Slide 8
Patient-Specific Quality Assurance (PSQA) - Ionization Chambers
PBS flat field scanning
Detector Placement
water
To accurately deliver the dose, quality assurance practices have to be done
Medical Dosimetry:
  Irradiating a particle detector with the treatment plan, to verify the delivered dose
Anode
Cathode
p-beam
e+ e-
High Voltage
Readout Circuit
C
R
Ionization Chamber
D: dose, E: energy, m: mass, Q: charge in detector, W: energy needed to create one electron/ion pair in air, s: stopping power

## Slide 9
Patient-Specific Quality Assurance (PSQA) - Ionization Chambers
PBS flat field scanning
Detector Placement
water
To accurately deliver the dose, quality assurance practices have to be done
Medical Dosimetry:
  Irradiating a particle detector with the treatment plan, to verify the delivered dose
30 cm
30 cm
PBS
Flat-panel detectors, made of segmented air cylinders, provide both dosimetry and dose map construction.
But with a limited resolution of ~ 6 mm

## Slide 10
Semiconductor-based Detectors
Semiconductor detectors are characterized by:
High radiation resistance
Increase image resolution ~ 0.2 mm
Fast acquisition and signal generation [5]
[5] N. Wyrsch and C. Ballif, “Review of amorphous silicon based particle detectors: The quest for single particle detection,” Semiconductor Science and Technology, vol. 31, no. 10, p. 103 005, 2016.
[6] H. Schindler, R. Veenhof, Garfield++ | simulation of ionisation based tracking detectors, 2018, URL http://garfieldpp.web.cern.ch/garfieldpp/
CMS Silicon Pixel Tracker
aSi Flat Panel Detectors
for X-ray Imaging

## Slide 11
Amorphous Silicon (a-Si) based TFT Flat Panel Detectors
a-Si Thin-Film-Transistor (TFT) Array consists of:
PIN Photodiode, which produced the current signal on the bottom electrode
Connects to the source of the TFT. When the insulating gate activates, the charges drift towards the drain and charge into a storage capacitor
Simulated in COMSOL, interfaced with Garfield++ [6], for understanding the specific characteristics of the pixel
photodiode
TFT
S
G
D
Data Lines
Gate
drivers
aSi TFT Array
[5] N. Wyrsch and C. Ballif, “Review of amorphous silicon based particle detectors: The quest for single particle detection,” Semiconductor Science and Technology, vol. 31, no. 10, p. 103 005, 2016.
[6] H. Schindler, R. Veenhof, Garfield++ | simulation of ionisation based tracking detectors, 2018, URL http://garfieldpp.web.cern.ch/garfieldpp/
p-doping
n-doping
Photodiode
Bias
Electrode
SiNx
gate
SiNx
a-Si
n+ a-Si
n+ a-Si
SiNx
Drain
Source
a-Si intrinsic layer
particle
-
-
-
-
+
+
+
+
TFT
Signal acquisition system

## Slide 12
Clinical Map 1
Clinical Map 2
Clinical Map 3
Improved resolution of Ionization Chambers to Silicon Pixel Detectors
Image acquired by
IBA MatriXX Resolution
Array of Ionization chambers

## Slide 13
Clinical Map 1
Clinical Map 2
Clinical Map 3
Improved resolution of Ionization Chambers to Silicon Pixel Detectors
Image acquired by
IBA MatriXX Resolution
Array of Ionization chambers
Images acquired by
IBA Sphinx Compact
aSi TFT Panel

## Slide 14
Comparison of small field dosimetry detectors
Proton beam gantry
Razor
aSi Pixels
To understand the different behavior of crystalline-based (c-Si) and amorphous-based (a-Si) silicon detectors under different particle beams.
The IBA Razor Diode and a small a-Si TFT array were irradiated with a flat 10 x 10 proton PBS with different doses.
Both diodes exhibited pristine charge linearity, without showing any saturation at high-proton doses.
Diodes will be further tested with proton and electron FLASH dose levels.
Dose Map of a flat 10 x 10 PBS field

## Slide 15
Comparison of small field dosimetry detectors
Proton beam gantry
To understand the different behavior of crystalline-based (c-Si) and amorphous-based (a-Si) silicon detectors under different particle beams.
The IBA Razor Diode and a small a-Si TFT array were irradiated with a flat 10 x 10 proton PBS with different doses.
Both diodes exhibited pristine charge linearity, without showing any saturation at high-proton doses.
Diodes will be further tested with proton and electron FLASH dose levels.
Dose Map of a flat 10 x 10 PBS field
Razor
aSi Pixels

## Slide 16
BACK-UP SLIDES

## Slide 17
Proton therapy delivery techniques – Conventional Scattering
Proton
Beam
Energy/Range
Modulator
Scatterer
Collimator
Compensator
Patient
Tumor
Irradiated Zone
A monoenergetic Proton Beam operates at the highest energy, while the modulator changes the energy per delivered dose. Where a compensator is placed, according to the shape of the tumor

## Slide 18
Silicon-based Pixel detectors
- Vbias
0 V
p+
n+ ohmic contact
n- bulk
depleted region
p-beam
-
-
-
+
+
+
Al
SiO2
neutral region
PN – Diodes
PIN – Diodes
p-doping
n-doping
Bias
Electrode
a-Si intrinsic layer
particle
-
-
-
-
+
+
+
+